PATIENT INSTRUCTIONS

Abduction Pillow Sling 			Bledsoe ARC Pillow Sling

ARC Pillow Info:

- Breathable extra padded fabric for greater comfort

- Encourages effective healing by allowing the shoulder and arm to remain in a neutral position.

- Helps prevent post-operative internal rotation

contractures that can occur in a sling.

- Promotes axillary air exchange to reduce risk of

secondary infections.

- Easy open front panel encourages forearm exercises.

Application Instructions:

- Detach waist strap and position elbow in the sling as far back as possible.

- Lift the strap over the patients head. Adjust the strap from the front by pulling to the desired tension.

- Adjust the neck pad to the desired position.

- Adjust the sling length by folding back the sling at the wrist.

- Adjust the Hand Grip. There are three tension straps: one on the bottom of the sling, and one on each side at the top of the sling.

- Detach and re-position the pillow with the shoulder in a neutral position. Secure by applying gentle pressure to the arm sling and the pillow.

Tips:

- Normally the sling will be most comfortable when the pillow is positioned right above the hip bone, sitting at approximately a 45 degree angle.

- Position the pad on the shoulder strap around the back of the neck to relieve any discomfort. Apply a small towel or washcloth under pad if it becomes too uncomfortable.

- Before removal of sling, place a small rolled-up towel in your affected-side armpit to help maintain the shoulder position.

- Use the buckle system to remove the sling.  This will eliminate the amount of readjustments to be performed each time it is removed and reapplied.

- Use your non affected arm to help support your affected side when removing the sling.

- Hand wash in cold water with mild detergent and air dry.