Post-Operative Knee Brace

Breg T Scope

Breg T Scope:

1

Straps engage and lock to brace uprights — stopping the leg within the proper range for safety.

2	Simple Hinge provides fast and easy adjustment with flexion limits of 0 to 120 and extension limits of 0 to 30° in 10° increments.

3	QuikLok mechanism enables rigid extension with a flip of two cam action levers.

Application Instructions:

1	Place the open brace under the affected leg.

2	Line the hinge up at the center of the knee, where the knee bends.  Be sure not to place the hinge too far forward or too far down the leg.

3	Loosely fasten straps.

4	Unlock strap lock clips and pull straps to remove slack behind the leg.

5	Maintain lateral and medial positions of the hinges.

6	Secure strap ends by hooking them onto opposite side of the brace.

7	Pull and adjust straps for a comfortable fit.

Simple Hinge Instructions:

1	Do not change ROM hinge unless instructed by your physician or physical therapist

2	Note the present limits by viewing the tabs visible on the hinge

3	Place the hinge in between the limits of desired motion before attempting to set the limits.

4	Pull the EXTENSION tab out and move until you reach the prescribed limit.  Now push tab in between the "teeth" to secure it.

5	Pull the FLEXION tab and move until you reach the prescribed limit.  Now push the tab in between the "teeth" to secure it.  The limits are now set.

6	The hinge may be locked by sliding the quick lock button into locked position at either 10* of hyperextension, full extension (0*), 10*, 20* or 30*.

Tips:

1	Remove and apply your brace with your leg flat on the floor in full extension..

2	Align the hinge to knee center first, then make sure bars are at the midpoint on each side of your leg.

3	The straps must be pulled snug to avoid sliding of the brace.

4	The foam pads and staps may be washed with cold water and mild detergent and air dried.