Patient Instructions

Motorized CryoTherapy Unit		Breg PolarCare 300

Cryotherapy Use:

- Apply immediately after surgery and wear at home during your recovery and rehab period.

- Use motorized cooler as instructed by your physician.

- Continue this product to control any pain and swelling. This recovery period is different for each individual.

- The cooling unit is a great tool to use in conjunction with your physical therapy. Do a 30 minute treatment before and after for best results.

Application Instructions:

- Position the pad toward the traumatized area of the body, bubble side down over the dressing or protective barrier.

- Fill cooler with ice to the “fill ice line.”  Add water and fill to same line.

- The blue tube should be positioned on the upper leg.

- Connect the blue tube and pad by pushing the connections together.

- Plug in the power supply to the wall outlet.

- To make the unit portable connect the hand bulb to the short hose on the top of the unit.  Depress the bulb 8-10 times to fill the pad, continue to depress the bulb every 10 minutes.

Tips:

- It is always best to have a protective barrier between the skin and the cooling pad.  A wash cloth or towel works very well.

- Water needs to be filled completely to the water line for best results.

- Check the ice level between uses.  When Ice needs to be added, reduce the water to the appropriate level.  Ice should last 6-8 hours.

- Drain the pad by depressing the 2 white buttons at the end of the blue tube.

Contraindications:

- Avoid using this cooling unit if you have any compromised circulatory or neurological deficiencies.

- Avoid using this product if you have Raynaud’s or other allergy to cold