Patient Instructions

CryoTherapy Unit							Aircast CryoCuff

Cryotherapy Use:

- Apply immediately after surgery and wear at home during your recovery and rehab period.

- Use cryotherapy unit as instructed by your physician.

- Continue using this product to control any pain and swelling. The recovery period is different for each individual.

- This cooling unit is a great tool to use in conjunction with your physical therapy. Do a 30 minute treatment before and after for best results.

Application Instructions:

- Connect blue tube to cooler, add water to the water line then add ice. Lay the insulated disk on top of ice and close the lid.

- Position the EMPTY cuff in the appropriate position.

- Raise the cooler no more than 15” above the cuff for approximately 30 seconds while the cuff fills.

- Correctly position cooler- place it on a stable surface, the base of the cooler should be even with the cuff.

- Turn cooler on- plug power supply into wall outlet and connect cord to lid.

- To refill cooler- when ice has melted, unplug the cooler and repeat the above steps.

Tips:

- It is always best to have a protective barrier between the skin and the cooling pad.  A wash cloth or towel works very well.

- A block of ice (freeze a half gallon container of water) or cubed ice will provide longer cold water temperatures

- Drain the cuff completely between use

- To avoid excessive pressure during use, do not raise the cooler higher than 15” above cuff

- Cooler cleaning- use mild detergent to clean cooler and lid as needed. Do not submerge lid under water

Contraindications:

- Avoid using this cooling unit if you have any compromised circulatory or neurological deficiencies.

- Avoid using this product if you have Raynaud’s or other allergy to cold