Patient Instructions

Gravity-Fed CryoTherapy Unit		                          Aircast CryoCuff

Cryotherapy Use:

- Apply immediately after surgery and wear at home during your recovery and rehab period.

- Use cryotherapy unit as instructed by your physician.

- Continue using this product to control any pain and swelling. The recovery period is different for each individual.

- This cooling unit is a great tool to use in conjunction with your physical therapy. Do a 30 minute treatment before and after for best results.

Application Instructions:

- Position the pad over the center of the knee with the knee cap aligned to the center of the pad; the valve should face up toward your thigh

- Fill cooler with water to the “fill ice line.”  Fill remainder of cooler with ice.

- Connect the blue tube and pad by pushing the connections together.

- Raise cooler above the level of the knee pad to fill pad with water.

- Disconnect tube or leave cooler level to pad during treatments.

- Every 30 minutes, lower cooler below pad to drain pad, shake cooler for a few minutes, then refill pad with the cold water

- To make the unit portable, disconnect the hose from the knee pad.

Tips:

- It is always best to have a protective barrier between the skin and the cooling pad.  A wash cloth or towel works very well.

- A block of ice (freeze a half gallon container of water) or cubed ice will provide longer cold water temperatures

- Drain the cuff completely between use

Contraindications:

- Avoid using this cooling unit if you have any compromised circulatory or neurological deficiencies.

- Avoid using this product if you have Raynaud’s or other allergy to cold