# Patient Instructions

Back Brace	                                                                             Corflex Disc Unloader

Disc Unloader Info:

- Unique modular design reduces intradiscal pressure through circumferential compression, standard 6" anterior and 12" posterior panels accept anatomically designed inserts along with gel pack that provides the benefits of cold/hot therapy

- Indicated for chronic or acute low back pain, discogenic disc disease, post-surgical application, strains/sprains to lumbar muscles/ligaments and postural support

- Constructed of soft breathable fabric with contoured rigid A.B.S. inserts, elastic double-pulls and contact closure support.

Application Instructions:

- Release Velcro closures, open orthosis and lay flat.

- Note: rigid inserts may be removed from pockets, heat molded to specifications, and reinserted or it may be used without inserts.

- Place anterior (low profile) panel on center of abdomen, making sure loop portion is facing outward and curve is facing down.

- Place posterior panel on center of back, making sure Corflex logo and elastic double-pulls are face outward.

- Grasp both ends of posterior panel, bring forward, and attach to loop on anterior panel.

- Grasp both ends of elastic double-pull, pull one side across and attach onto loop area on opposite side of posterior panel, pull other side across and attach to loop area on opposite double-pull.

- Adjust to desired tension, making sure not to over tighten.

Tips:

- Close all contact closures and hand wash in warm water with mild soap. Product should be air-dried, do not use high temperatures to wash or dry.