| Custom Osteoarthritis Unloader | For Medial or Lateral Compartment Arthritis |
| --- | --- |

About your Custom OA Unloader Knee Brace:

- 3-Point leverage system proven to provide pain relief.

- Adjustable Dynamic Joint – An Adjustment Mechanism that allows the clinician to fine tune the varus or valgus force needed for optimum pain relief.

- The Dynamic Force Strap – This carefully designed strap applies a counteracting force at the adduction moment, considered to be the root cause of Knee Osteoarthritis.

- Low-profile design, able to fit comfortably underneath most clothing.

- Custom carbon shell is strong yet flexible, while its featherweight materials make it a choice for activities of daily living.

- Custom made to individual patient measurements.

- Replacement liners and strap pads available.

- Color Choices Available.

Application Instructions:

- While sitting on the edge of a chair, fully extend the knee.

- Center the middle of the hinge with the top of the kneecap and position calf shell flush with skin.

- Secure the upper calf strap, then the lower calf strap.

- Keeping the knee fully extended, position thigh shell flush with the skin.  Continue to strap the lower thigh strap, followed by the upper thigh strap.

- The Dynamic Force Strap™ (DFS) - Wrap the strap around the back of your leg and thread it through the strap ring on the thigh shell. Bend your braced knee to an angle of approximately 80 degrees. While holding the thigh shell, to prevent the brace from moving, tighten the DFS. The DFS should be worn snug for maximum pain relief.

- When all strapping is complete, the hinge should center just above the top of the kneecap and slightly behind the midline.

- Call your Orthocare clinician before making any varus or valgus unloading adjustments (603) 644-0774.

Tips:

- Tighten straps snugly, but comfortably.  After 15 minutes of activity, loosen, then re-tighten all straps in proper order.  This is required because of tissue swelling and compression.

- Watch for any skin irritation or rubbing of the brace.  You may also experience a skin rash, which may mean you are allergic to the strap pads and liners.

- Straps and pads may be removed and cleaned.  Hand wash straps and pads in cold water with mild detergent, air dry. The hinge requires little maintenance with normal use.  Occasionally apply a dry lubricant, especially after use in water.  If used in salt water, be sure to rinse hinges with fresh water to avoid corrosion.